## Slide 1
Status of Calorimeter R&D from PHENIX
EIC Calorimeter Group Meeting
December 5, 2013
S.Beckman¹, S.Boose, J.Haggerty, E.Kistenev, C.Pinkenberg, S.Stoll, C.Woody, L.Xue²
¹ University of Colorado grad student
² Georgia State University

## Slide 2: EMCAL Tilted Plate Configuration (Flat plates - No Accordion)
L.Xue
Tilt angle = 6.16°

## Slide 3: New EMCAL Prototype
Test stack of 7 tower modules (not yet glued)
Prototype will have 7x7 optically separated towers
1 mm (2 x 0.5 mm) flat W plates, 1 mm fibers, rear spacer for tapering
S. Stoll, W.Lenz & K.Jones

## Slide 4
EMCAL Prototype Assembly
Epoxy is applied to 2 tungsten plates
Twelve sandwiches are glued together to form a module
Readout end of module is potted with white reflecting epoxy. Other end is covered with 3M ESR reflector
Plates and fiber layer are glued together under vacuum to form a “sandwich”

## Slide 5
Light Collection Cavities
Row of 7 cavities for testing SiPM placement
SiPMs are mounted to small PCB and connected to a carrier board with shielded wires

## Slide 6: Connection to Readout Electronics

## Slide 7
Light Collection Efficiency
S. Stoll
Average efficiency = 4.7%
Max/Min ratio = 1.7

## Slide 8
Light Yield
Light output from absorber stack was measured with cosmic rays for one tower module (12 scintillator layers) with directly coupled PMT
Light yield from stack = 600 g/MeV (energy deposited in scintillator)
Sampling fraction of 6.4%
 38,400 g/GeV in calorimeter
Light collection efficiency of 4.7% from cavities  1800 g/GeV
SiPM PDE = 35%
 630 p.e./GeV
 4% contribution to energy
resolution from photon statistics
Light Yield = 600 g/MeV
S. Stoll

## Slide 9
Laser Calibration System
Splitter fixture for testing uniformity/ efficiency
of 1x7 splitters
1x7 splitter for distribution of laser calibration
light to light collection cells
PiLas laser
photodiode
1:2 split
1:7 split
1:7 split

## Slide 10
HCAL Prototype
Being assembled in the HiBay in Physics

## Slide 11
Testing of Calorimeter Components at Colorado
S.Beckman
Light output and uniformity measurements of scintillating tiles
Top fiber
Light Yield ~ 18 p.e./”mip” (measured with 90Sr)
Bottom fiber

## Slide 12
Fermilab Beam Test
Test of combined EMCAL and HCAL prototypes scheduled for Feb 5-25, 2014

## Slide 13: Future R&D Plans
Test 7x7 prototype in test beam at Fermilab (electrons up to ~ 8 GeV)
Test 7x7 prototype in test beam at SLAC to obtain better measurement of energy resolution (electrons up to ~ 15 GeV)
Continue development of thin W plates with THP
  Produce larger plates (~ 1 m) and determine achievable tolerances
  Determine if it is possible/cost effective to produce tapered plates
  Determine if it is possible/cost effective to produce accordion shaped plates
Build large scale (~ 1m long) prototype module
  Develop technique for assembly aimed at industrialized process
  Develop technique for fiber layout to make fully projective towers
Test new SiPMs from Hamamatsu
Continue development of readout system and electronics

## Slide 14: Budget for Future R&D Plans